## Slide 1
Definitions
Event (E) – one of 8 Darpa’s defined scenarios
Mission – a part of an event
Task (T) – one of 7 groups defined in the proposal
Task
T 1 | Operation
T 2 | Perception
T3 | Decision Making
T4 | Dismounted Mobility
T5 | Mounted Mobility
T6 | Dexterity
T7 | Integration
Event
E 1 | Drive a utility vehicle at the site
E 2 | Travel dismounted across rubble
E3 | Remove debris blocking an entryway
E4 | Open a door and enter a building
E5 | Climb an industrial ladder and traverse an industrial walkway
E6 | Use a tool to break through a concrete panel
E7 | Locate and close a valve near a leaking pipe
E8 | Replace a component such as a cooling pump

## Slide 2
Capabilities / Modules
Locomotion and Stability
  Keep stable and perform maneuvers to remain stable
  Go forward, left etc.
Posture Control
  Maintain stable posture
Body Control
  Move arms, head and body
Vision and
  Operate camera and
Mission planning
  Plan how to complete mission
Mission execution
  sequencer
Operator control
  Intervention in decision making (T3) processes.
  Event execution
Health Monitoring
  Monitor robot state, power, communication, time
Scene Recognition
  Ground mapping
  Objects mapping
Object recognition
  Identification and classification of objects
Obstacle Detection
  Detect obstacles on ground and above
Global Position
  Robot’s position in world coordinates
Local Body Position
  All links positions
Global Path Planning
  Find best path to target using a-priori knowledge
Local Path Planning
  Find local path using sensed environment
Climb a ladder
Move an Object
  Moving/ pushing debris
Open a Door
Operate a Tool
Replace Pump
Close Valve
Car operation
  Pedals
  Car ignition
  steering wheel
  Gear
Mount Vehicle
Dismount Vehicle
T4
T4
T2
T3
T3
T1
T7
T2
T2
T2
T2
T3
T3
T6
T4
T6
T4
T6
T6
T5
T6
T4
T4
T4

## Slide 3
Control requirements from Modules
Transmit a confirmation for receiving commands from other modules.
Transmit a confirmation for sending commands to other modules.
Provide an estimate for completion time.
Implement an immediate termination command and a safe termination command (i.e. stop only after guarantied safety).
Transmit state signal for successful execution or unsuccessful one (and what went wrong).

## Slide 4
First Test Event
Implement a simple walking event to a any humanoid in Gazebo.
Locomotion and Stability
Mission planning
Mission execution
Global Position
Local Body Position
Global Path Planning
Operator control